## Slide 1: Introduction
Overview. What is the Internet? What is a protocol?
Network edge
Network core
Performance: loss, delay, throughput
Protocol layers, service models
Security
History
COMPSCI 453 Computer Networks
Professor Jim Kurose
College of Information and Computer Sciences
University of Massachusetts
Class textbook:
Computer Networking: A Top-Down Approach (8th ed.)
J.F. Kurose, K.W. Ross
Pearson, 2020
http://gaia.cs.umass.edu/kurose_ross

## Slide 2: Chapter 1: introduction
Chapter goal:
Get “feel,” “big picture,” introduction to terminology
  more depth, detail later in course
Overview/roadmap:
What is the Internet? What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Protocol layers, service models
Security
History

## Slide 3: What is the Internet?
https://www.youtube.com/watch?v=ourb9j-dq8Q
https://www.youtube.com/watch?v=iDbyYGrswtg

## Slide 4: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 5: “Fun” Internet-connected devices
Web-enabled toaster +
weather forecaster
Internet phones
Slingbox: remote
control cable TV
Security Camera
IP picture frame
Internet
refrigerator
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress
Amazon Echo
Others?
Pacemaker & Monitor
AR devices
Fitbit
Gaming devices
cars
scooters
bikes

## Slide 6: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force

## Slide 7: The Internet: a “services” view
Infrastructure that provides services to applications:
  Web, streaming video, multimedia teleconferencing, email, games, e-commerce, social media, inter-connected appliances, …
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
provides programming interface to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to, use Internet transport service
  provides service options, analogous to postal service

## Slide 8: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events

## Slide 9: What’s a protocol?
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 10: Introduction
Introduction. What is the Internet? What is a protocol?
Network edge
Network core
Performance: loss, delay, throughput
Protocol layers, service models
Security
History
COMPSCI 453 Computer Networks
Professor Jim Kurose
College of Information and Computer Sciences
University of Massachusetts
Class textbook:
Computer Networking: A Top-Down Approach (8th ed.)
J.F. Kurose, K.W. Ross
Pearson, 2020
http://gaia.cs.umass.edu/kurose_ross
Video: 2020, J.F. Kurose, All Rights Reserved
Powerpoint: 1996-2020, J.F. Kurose, K.W. Ross, All Rights Reserved